## Slide 1: Advanced Driver Assistance System

## Slide 2: Outline
Business context
Use cases
Constraints
Quality requirements
Software architecture
Satisfying requirements
Prepare for the next iteration

## Slide 3: Business context
!Crash is an automotive supplier in the driver assistance product area supplying lane-keep and object detection features for cars, with over 1 million products deployed in various cars and trucks.
!Crash base technology is radar, ultrasonic and image recognition using machine learning where possible.

## Slide 4: Business context
There are many challenges with sensor fusion and real-time responses in these products.
Their product is often integrated with software from their customers as well as their product must interact with many other products within the vehicle to accomplish features for the driver.

## Slide 5: Basic functionality
Automatic Forward and Reverse Braking
  Their product provides information (the existence of impending objects of threat to the vehicles’ forward or reverse progress) that can be used in the determination of a need to halt, or redirect, the progress of the vehicle.

## Slide 6: Basic functionality
Multiple sensor technologies are utilized in real time to identify objects and perform a threat analysis.
Timely determination of objects and threats is critical to the useful functionality of their product.

## Slide 7: Outline
Business context
Use cases
Constraints
Quality requirements
Software architecture
Satisfying requirements
Prepare for the next iteration

## Slide 8: UC - Back out of a Parking space
The vehicle driver is backing the vehicle out of a parking space with potential cross traffic to avoid. For the identified “objects” that pose the greatest risk, a determination of driver or automated vehicle response is made and acted upon. These may be passive (inform driver) or active (override driver and command the vehicle). Override options are to temporarily stop the car until threat is gone or pull car back into parking space.

## Slide 9: Outline
Business context
Use cases
Constraints
Quality requirements
Software architecture
Satisfying requirements
Prepare for the next iteration

## Slide 10: Constraint 1
This product does not INCLUDE any o the sensors, it interfaces with Radar, Ultrasonic and Image processors (that do their own ML)

## Slide 11: Constraint 2
Autonomous acceleration and steering angles are limited to AL and SL. These are provided by the Vehicle OEM.

## Slide 12: Constraint 3
The system must interact with smart sensors from 3rd party suppliers as well as steering, brake and powertrain controllers in the vehicle over CAN bus (controller area network).

## Slide 13: Constraint 4
If the system contradicts the actions of the driver, the driver must be informed and the event logged with the external “monitoring element” in the vehicle.

## Slide 14: Constraint 5
The vehicle will have a token based authorization method such as Kerberos available.

## Slide 15: Outline
Business context
Use cases
Constraints
Quality requirements
Software architecture
Satisfying requirements
Prepare for the next iteration

## Slide 16: Performance requirement
For this use case, the assumption is a maximum 75MPH of external object speed. This requires all sensor captures, fusion, classification, threat determination and initiation of vehicle recourse occur before the object has moved one foot, in this case 1.5 seconds.

## Slide 17: Reliability requirement
Given scenarios of similar circumstances (same number and characteristics of objects, categories and velocities) system performance needs to react consistently greater than 90% of event trials. If any single step in flow cannot make a determination, driver must be made aware of system inoperability within .25 seconds of said determination.

## Slide 18: Availability requirement
If any single step in flow cannot make a determination, driver must be made aware of system inoperability within .25 seconds of said determination.

## Slide 19: Scalability requirement
The system should perform with up to 10 objects of potential threat recognized.

## Slide 20: Security requirement
System is connected via CAN bus to elements with telematic connectivity and therefore shall be protected from unauthorized CAN messages.
Machine Learning Training data should build a model sufficient enough to determine 2D from 3D objects to avoid the use of image spoofing.

## Slide 21: Observability requirement
The Driver must be aware of the moment the system takes command of the vehicle from their control, or if the system is unable to take command and the driver must take action.

## Slide 22: Modifiability requirement
Support for additional Radar, Lidar or Camera sensors must be achievable within a 6 month development cycle of the team.

## Slide 23: Outline
Business context
Use cases
Constraints
Quality requirements
Software architecture
Satisfying requirements
Prepare for the next iteration

## Slide 24: Modules
Tracking objects
Recourse decision
Threat Analysis
Vehicle boundary
Sensor Fusion
System monitor
External software elements
Can Bus

## Slide 25: Tracking Objects
Gets Data from smart sensors
Passes object data to Sensor Fusion

## Slide 26: Sensor Fusion
Compares object data and locations
Aggregates and formulates definitions of objects and their data set
  Category, location, size, velocity
Provides summary field of objects for Threat Analysis

## Slide 27: Vehicle Boundary
Fixed calibration data of particular vehicle to which product is installed is provided at OEM production line
  Vehicle dimensions, center points
Element calculates the center position of vehicle and its absolute global position from CAN data provided by other elements.
  Calculates the volume in global points the vehicle (that on which the product is installed) occupies.

## Slide 28: Threat Analysis
Takes in Object field from Sensor Fusion and vehicle location and volume from Vehicle Boundary
  Calculates risk probability for up to 10 objects
Communicates risk data and object data to Recourse Decision element

## Slide 29: Recourse Decision
Recalculates probability ranking from last run with new data from Threat Analysis
Determines if recourse is required
  Makes choice of active or passive recourse
  Executes recourse

## Slide 30: System Monitor
This element monitors communication on CAN bus to determine performance, reliability, and availability of the system.

## Slide 31: CAN Bus
A Controller Area Network (CAN bus) is a robust vehicle bus standard designed to allow microcontrollers and devices to communicate with each other's applications without a host computer.

## Slide 32: Packaging of modules
Package each module in module view as service
This allows allocation of services to ECUs to be different for different OEMs

## Slide 33: Outline
Business context
Use cases
Constraints
Quality requirements
Software architecture
Satisfying requirements
Prepare for the next iteration

## Slide 34: Steps in achieving use case
Determine what is back there
  Tracking Objects will identify stationary and approaching “objects” into defined object categories and gross physical size dimensions.
2. Where is it?
  For the identified “objects” Sensor Fusion will provide geo-location information and velocity.

## Slide 35: Steps in achieving use case
3. Is it a Problem?
  For the identified “objects”, and their category, size, velocity and location Threat Analysis will determine a level of threat regarding a collision with the reversing vehicle.
4. What can be done about it?
  For the identified “objects” that pose the greatest risk, Recourse Decision makes and acts on either a driver or automated vehicle response

## Slide 36: Satisfying Constraint 1
This product does not INCLUDE any o the sensors, it interfaces with Radar, Ultrasonic and Image processors (that do their own ML)
  Tracking Objects gets data from CAN bus.

## Slide 37: Satisfying Constraint 2
Autonomous acceleration and steering angles are limited to AL and SL. These are provided by the Vehicle OEM.
  This information is placed into a location known to the Recourse Decision element when the vehicle is on the production line

## Slide 38: Satisfying Constraint 3
The system must interact with smart sensors from 3rd party suppliers as well as steering, brake and powertrain controllers in the vehicle over CAN bus.
  Tracking Objects gets data from the CAN bus
  Recourse Decisions sends messages to the CAN bus

## Slide 39: Satisfying Constraint 4
If the system contradicts the actions of the driver, the driver must be informed, and the event logged with the external “monitoring element” in the vehicle.
  Recourse Decision does this over the CAN bus.

## Slide 40: Satisfying Constraint 5
The vehicle will have a token-based authorization method such as Kerberos available.
  All elements in the system authorize using token-based authorization mechanism

## Slide 41: Performance requirement
For this use case, the assumption is a maximum 75MPH of external object speed. This requires all sensor captures, fusion, classification, threat determination and initiation of vehicle recourse can occur before the object has moved one foot, in this case 1.5 seconds.
  This requirement is shared among elements in satisfying use case

## Slide 42: Reliability requirement
Given scenarios of similar circumstances (same number and characteristics of objects, categories and velocities) system performance needs to react consistently greater than 90% of event trials. If any single step in flow cannot make a determination, driver must be made aware of system inoperability within .25 seconds of determination.
  System monitor does this

## Slide 43: Availability requirement
If any single step in flow cannot make a determination, driver must be made aware of system inoperability within .25 seconds of said determination.
  System monitor does this

## Slide 44: Scalability requirement
The system should perform with up to 10 objects of potential threat recognized.
  This requirement is shared among elements

## Slide 45: Security requirement
System is connected via CAN to elements with telematic connectivity and therefore shall be protected from unauthorized CAN messages.
  System uses token authorization mechanism such as Kerberos.

## Slide 46: Security requirement
Machine Learning Training data should build a model sufficient to determine 2D from 3D objects to avoid the use of image spoofing.
  This testing is done in the development phase

## Slide 47: Observability requirement
The Driver must be aware of the moment the system takes command of the vehicle from their control, or if the system is unable to take command and the driver must take action.
  The System Monitor does this

## Slide 48: Modifiability requirement
Support for additional Radar, Lidar or Camera sensors must be achievable within a 6 month development cycle of the team.
  This is delegated to the Tracking Objects and Sensor Fusion